## Slide 1
IoT-Based Smart Waste Management System with Reward System

## Slide 2: Team : 01
Member 1:
MAHFUZ ANAM
Roll : 374
Exam Roll : 202186
Member 2:
S.I.M. ADNAN
Roll : 378
Exam Roll : 202190
Member 3:
TAUFIQ ISLAM
Roll : 384
Exam Roll : 202196

## Slide 3: TABLE OF CONTENTS
1.Project Overview
2. Features
3. Hardware Components
4. Software Components
5. System Operation Workflow
6. Flowchart
7. Circuit Diagram
8. Website Interface
9. Mobile App Interface
10.Conclusion

## Slide 4: Project Overview
IoT- Integrated Smart Bin: Uses ESP32, sensors, and servo for automated waste disposal.
RFID Access: Ensures secure, user-specific waste tracking.
Reward Points: Users earn points for responsible disposal.
Web & IoT Dashboard: Blynk and Web interface enable remote monitoring.

## Slide 5: Features
RFID-based User Authentication
  Ensures only registered users can dispose of waste.
  Tracks individual user activity for rewards.
Automated Lid Operation
  Opens lid automatically after successful RFID scan.
  Touchless and hygienic waste disposal.
.

## Slide 6: Features
Real-time Fill Level Detection
  Ultrasonic sensors measure waste level continuously.
Reward System
  Awards points based on waste deposited.
  Motivates responsible disposal
Monitoring via web interface
  Accessible through web interface and mobile app.

## Slide 7: HARDWARE COMPONENTS
ESP32 Microcontroller
Ultrasonic Sensors (HC-SR04) (2)
RFID Reader(MFRC522)
Servo Motor(SG90)
Power Supply

## Slide 8: SOFTWARE COMPONENTS
C++ with Arduino IDE for embedded software
HTML, CSS, React.js for web interface
Blynk for IoT data handling

## Slide 9: SYSTEM OPERATION FLOW
Idle State
  Waits for RFID scan.
RFID Scan
  Reads user card.
Authentication
  Valid card → proceed.
  Invalid card → show error, return idle.
Lid Control
  Opens lid for 7 seconds.
  Closes lid automatically.
Fill Level Check
  Measures waste level before and after disposal.
Reward Allocation
  Increase ≥1cm → award 10 points.
  Else → no points.
Data Update
  Update reward points and waste level.
  Send data to IoT platform.
Reset
  Return to idle state.

## Slide 10: FLOWCHART

## Slide 11: CIRCUIT DIAGRAM

## Slide 12: WEBSITE INTERFACE

## Slide 13: WEBSITE INTERFACE

## Slide 14: MOBILE APP INTERFACE

## Slide 15: Conclusion
The system improves waste management efficiency through real-time monitoring and automation.
The reward mechanism encourages user participation and promotes responsible disposal.
The scalable IoT platform enables remote monitoring and potential city-wide deployment.

## Slide 16
THANK YOU
ANY QUESTIONS??